## Slide 1
MIMO Based Radio-over-Fiber link for Millimeter Wave Generation Using an External Optical Modulator

## Slide 2
Our Team
Nafis Fuad Barshan
Reg:21201166
Tanvir Rahan Rifat
Reg:22101065
Taohid Khan
Reg:22101070

## Slide 3
Introduction
Millimeter-wave (mm-wave) communication, with its extensive bandwidth capabilities, has become critical for addressing the growing demands of high-speed data networks. Combining Multiple Input Multiple Output (MIMO) technology with Radio-over-Fiber (RoF) systems enables reliable and long-distance communication with minimal signal degradation. Despite its promise, conventional RoF systems face challenges like optical power loss and modulation inefficiency, necessitating innovative design solutions.

## Slide 4
In this paper, our primary contribution lies in presenting a low-complexity yet high-performance MIMO-RoF system design that addresses existing bottlenecks in signal transmission and modulation efficiency. This work provides a theoretical basis for future implementations in next-generation wireless communication networks.
This paper focuses on a novel approach for mm-wave generation using advanced external optical modulators in a 2×2 WDM-enabled MIMO-RoF framework. The proposed system introduces precise signal processing techniques and enhanced wavelength multiplexing to minimize distortion while achieving optimal spectral efficiency.

## Slide 5
Problem Statement
Low Frequency, high coverage
High Frequency, low coverage
High Noise
Using wrong components
Optical power loss
Modulation Inefficiency

## Slide 6
Figure: (a) Amplitude-Modulator-based-RoF-link

## Slide 7
Figure: (b) Dual-Drive-MZM-based-RoF-link

## Slide 8
Literature Review
1
MIMO and Radio-over-Fiber Systems
Multiple-Input Multiple-Output (MIMO) systems have revolutionized wireless communication by significantly enhancing spectral efficiency, data rates, and network reliability.
2
Optical Modulators for Millimeter-Wave Signal Generation
Optical modulators are indispensable components of RoF systems, converting electrical signals into optical signals to facilitate the transmission of mm-wave signals over optical fibers.
3
Challenges in MIMO-Based RoF Systems
Despite their numerous advantages, MIMO-RoF systems face several technical challenges: Optical Power Loss, Signal Distortion, and Scalability.

## Slide 9
System Design
Model 1: Amplitude Modulator-Based MIMO-RoF System
This model demonstrates a MIMO-RoF system employing Amplitude Modulators (AM) to generate and transmit millimeter-wave signals.
Transmitter Side
Fiber Link
Receiver Side
Model 2: Dual-Drive Mach-Zehnder Modulator (DD-MZM) Based MIMO-RoF System
This model uses DD-MZMs for enhanced performance in generating and transmitting millimeter-wave signals.
Transmitter Side
Fiber Link
Receiver Side

## Slide 10
Results & Discussion
S/No.
Devices (Model Number)
Parameter
Values
1
NRZ & RZ Pulse Generator
Rectangle Shape
Exponential
Amplitude
1 a.u.
3
Amplitude Modulator
Modulation Index
1
4
Dual Port Dual Drive Mach Zehnder Modulator (MZM)
Splitting Ratio
1.3
5
Optical Fiber
Length
5m
Optical Fiber
Attenuation
0.2dB/km
Dispersion
16.75 ps/nm/km
Differential Group Delay
0.5 ps/km
6
Fiber Bragg Grating
Length
2mm
Effective index
1.45
Frequency
1552.52nm
7
Photodetector PIN
Responsivity
1A/W
8
Dark Current
10nA
Low pass Bessel Filter
Cutoff Frequency
0.75\*Bit Rate Hz
2

## Slide 11
Chart: 
| Optical Spectrum Analyzer | Optical Power Meter (EDFA) | Optical Spectrum Analyzer | Optical Time Domain Analyzer (Max) | Optical Time Domain Analyzer (Min) | Eye Diagram 1 | Eye Diagram 2
AM Based RoF Link 23.647 | -20.922 | 17.027 | 15.5 | 0.77 | -0.03 | 6.17 | 6.56
DD-MZM Based RoF Link N/A | -17.273 | 17.186 | 17.83 | 0.34 | -0.01 | 2.4184 | 2.397
Result representation

## Slide 12
Results
FIGURE 1. Optical Power Spectrum of RoF link using AM: (a) frequency domain; (b) time domain & (c) Power Meter

## Slide 13
FIGURE 2. Optical Power Spectrum of RoF link using Dual drive MZM: (a) frequency domain; and (b) time domain
Results

## Slide 14
FIGURE 3. (a) RF Power Spectrum of AM-based design (b) RF Power Spectrum of Dual drive MZM-based design
Results

## Slide 15
Results
FIGURE 5. Constellation Visualizer output: (a) RoF link with AM; and (b) RoF link with DD-MZM

## Slide 16
System Design:
  Developed two MIMO-RoF models using OPTISYSTEM software: a) Amplitude Modulator (AM)-based. b) Dual-Drive Mach-Zehnder Modulator (DD-MZM)-based.
  Key components include pseudo-random bit sequence generators, modulators, WDM MUX/DEMUX, optical fibers, and photodetectors.
Simulation:
  Conducted simulations to analyze optical and RF spectra, signal integrity, and modulation performance.
  Evaluated systems on Q-factor, Bit Error Rate (BER), and spectral efficiency.
Methodology

## Slide 17
3.Comparison:
  Assessed AM and DD-MZM-based systems for sideband suppression, power efficiency, and signal distortion.
4.Results:
  Demonstrated feasibility for high-frequency mm-wave generation in 5G networks and beyond.

## Slide 18
Conclusion
This study presents a comprehensive modelling of a 2×2 MIMO-based Radio-over-Fiber (RoF) system for millimeter-wave generation, utilizing two distinct optical modulators.
Dual-Drive Mach-Zehnder Modulator (DD-MZM) efficiently generates high-frequency signals with multiple power peaks, achieving frequencies up to 60 GHz.
The Amplitude Modulator (AM)-based RoF link achieves a Q-factor of 4 to 6,with so much noise and Bit Error Rate (BER) over a 0.5 km optical fiber.
This work highlights the potential of tailored MIMO-based RoF systems in addressing the growing demands for high-frequency, high-capacity, and low-latency communication networks.

## Slide 19
Thank
You